## Slide 1
WIPRO NGA Program – 25SUB4505_5 G Developer
Capstone Project Presentation – 13th Feb 2026
www.rpsconsulting.in
Presented by – Group (03)
Project Title Here – 5G NR RLC ARQ Process
WIPRO NGA Program – 25SUB4505_5 G Developer
Capstone Project Presentation – 13th Feb 2026
www.rpsconsulting.in
Presented by – Group (03)
Project Title - Test 9: Physical Layer - HARQ Operation

## Slide 2
2024 - RPS Consulting all rights reserved
PDCP LAYER
Security and Header Compression
5G NR Protocol Stack Implementation
HARQ OPERATION
(Physical Layer)
Hybrid Automatic Repeat Request in 5G New Radio
3GPP TS 38.321 | TS 38.214

## Slide 3
2024 - RPS Consulting all rights reserved
What is HARQ ?
Hybrid Automatic Repeat Request (HARQ)
A core reliability mechanism in 5G NR that combines Forward Error Correction (FEC) with feedback-driven retransmissions to ensure robust data delivery over unreliable wireless channels.
→
Cross-Layer Operation
Integrates Physical Layer (TS 38.214) and MAC Layer (TS 38.321)
↻
Incremental Redundancy
Progressive parity injection instead of simple retransmission
⚡
Low Latency Design
Parallel HARQ processes enable continuous data flow

## Slide 4
2024 - RPS Consulting all rights reserved
4
HARQ In 5G NR Protocol Architecture
MAC Layer (TS 38.321)
• HARQ process allocation
• NDI management
• Feedback timing
• Retransmission control
Physical Layer (TS 38.214)
• Channel coding & rate matching
• RV selection
• Soft combining
• ACK/NACK generation
WHY THIS ARCHITECTURE?
✓
Parallel HARQ processes minimize idle time
✓
Asynchronous operation enables flexible scheduling
✓
Supports eMBB, URLLC, and mMTC use cases
✓
Maintains high throughput with low latency

## Slide 5
2024 - RPS Consulting all rights reserved
Physical Layer Overview
Layer 1 converts higher-layer data into radio signals and vice versa, handling transmission procedures, coding, modulation, and HARQ-related operations as specified in 3GPP TS 38.214.
◈
Channel Coding
FEC encoding and rate matching
↻
HARQ Procedures
RV selection & soft combining
◉
Modulation
QPSK, 16QAM, 64QAM, 256QAM
⇄
Feedback Generation
ACK/NACK decision
▦
Resource Mapping
Time-frequency allocation
◭
Flexible Numerology
Scalable subcarrier spacing

## Slide 6
2024 - RPS Consulting all rights reserved
HARQ Process Architecture
Process P0
IDLE
Process P1
WAIT_ACK
Process P2
RETRANSMIT
Process P3
SUCCESS

## Slide 7
2024 - RPS Consulting all rights reserved
NDI : New Data Indicator
NDI acts as the identity switch for a HARQ process, distinguishing a new Transport Block from a retransmission of an earlier one.
NDI TOGGLED
New Transport Block
• Receiver resets combining buffer
• Prepares to decode fresh data
• Process identity changes
• RV resets to 0
NDI UNCHANGED
Retransmission
• Same Transport Block
• Receiver performs soft combining
• Merges with previous attempts
• RV increments for new parity
⚡ NDI ensures transmitter and receiver stay synchronized on data identity

## Slide 8
2024 - RPS Consulting all rights reserved
RV Cycling : Progressive Redundancy
The Redundancy Version (RV) controls which coded bits are transmitted in each HARQ attempt. Instead of repeating the same bits, the system progressively injects new parity information with every retransmission.
RV=0
RV=2
RV=3
RV=1
↻
Each retransmission adds NEW decoding information
⚡
No wasted bandwidth on blind repetition
✓
Progressive refinement increases success probability

## Slide 9
2024 - RPS Consulting all rights reserved
ACK/NACK : Closed – Loop Control
RV=0
RV=2
RV=3
RV=1

## Slide 10
2024 - RPS Consulting all rights reserved
Soft Combining : Accumulating Reliability
Instead of discarding failed transmissions, the receiver stores probability-level information (Log-Likelihood Ratios) from each attempt and merges it with new information from retransmissions. With each combining step, confidence increases.
CONFIDENCE INCREASE WITH EACH RETRANSMISSION
Attempt 1
40%
Attempt 2
65%
Attempt 3
85%
Attempt 4
98%
• Each transmission contributes new knowledge
• Probability information accumulates in soft buffer
• Incremental redundancy ensures efficient use of retransmissions

## Slide 11
2024 - RPS Consulting all rights reserved

## Slide 12
2024 - RPS Consulting all rights reserved
Retransmission Logic & Failure Resolution

## Slide 13
2024 - RPS Consulting all rights reserved
Snippet
// HARQ Process Simulation - TS 38.321 §5.4
#include <iostream>
#include <vector>
#include <cstdint>
#include <string>
#include <array>
#include <random>
struct HARQProcess {
int id;
bool ndi = false; // New Data Indicator
int rv = 0; // Redundancy Version (0,2,3,1 cycle)
int retx_count = 0;
int max_retx = 4;
bool active = false;
std::string data;
static const std::array<int, 4> rv_sequence;
Code
Output
HARQ ID: 1
NDI: 0
RV: 0
Retx Count: 0

## Slide 14
2024 - RPS Consulting all rights reserved
Snippet
void new_transmission(const std::string& d) {
data = d; ndi = !ndi; rv = 0; retx_count = 0; active = true;
std::cout << " HARQ[" << id << "] NEW TX: NDI=" << ndi
<< " RV=" << rv << " data=\"" << data << "\"\n";
}
bool retransmit() {
if (retx_count >= max_retx) {
std::cout << " HARQ[" << id << "] MAX RETX reached!\n";
active = false; return false;
}
retx_count++;
rv = rv_sequence[retx_count % 4];
std::cout << " HARQ[" << id << "] RETX #" << retx_count
<< ": RV=" << rv << "\n";
return true;
}
Code
Output
HARQ[1] NEW TX: NDI=1 RV=0 data="Hello"
HARQ[1] RETX #1: RV=2
HARQ[1] RETX #2: RV=3
HARQ[1] RETX #3: RV=1
HARQ[1] RETX #4: RV=0
HARQ[1] MAX RETX reached!

## Slide 15
2024 - RPS Consulting all rights reserved
Snippet
void ack() {
std::cout << " HARQ[" << id << "] ACK received\n";
active = false;
}
};
const std::array<int, 4> HARQProcess::rv_sequence = {0, 2, 3, 1};
int main() {
std::cout << "=== HARQ Process (TS 38.321 §5.4) ===\n\n";
std::cout << "16 parallel stop-and-wait HARQ processes\n";
std::cout << "RV sequence: 0 -> 2 -> 3 -> 1\n\n";
std::mt19937 rng(42);
HARQProcess proc{0};
proc.new_transmission("PDU-DATA-A");
Output
Code
===HARQ Process (TS 38.321 §5.4) ==
16 parallel stop-and-wait HARQ processes
RV sequence: 0 -> 2 -> 3 -> 1
HARQ[0] NEW TX: NDI=1 RV=0 data="PDU-DATA-A"

## Slide 16
2024 - RPS Consulting all rights reserved
Snippet
// Simulate NACK (channel error)
std::cout << " << NACK (CRC fail) >>\n";
proc.retransmit();
std::cout << " << NACK >>\n";
proc.retransmit();
std::cout << " << ACK (combining success) >>\n";
proc.ack();
std::cout << "\n";
proc.new_transmission("PDU-DATA-B");
std::cout << " << ACK (first attempt) >>\n";
proc.ack();
return 0;
}
Output
Code
=== HARQ Process (TS 38.321 §5.4) ===
16 parallel stop-and-wait HARQ processes
RV sequence: 0 -> 2 -> 3 -> 1
HARQ[0] NEW TX: NDI=1 RV=0 data="PDU-DATA-A"
<< NACK (CRC fail) >>
HARQ[0] RETX #1: RV=2
<< NACK >>
HARQ[0] RETX #2: RV=3
<< ACK (combining success) >>
HARQ[0] ACK received
HARQ[0] NEW TX: NDI=0 RV=0 data="PDU-DATA-B"
<< ACK (first attempt) >>
HARQ[0] ACK received

## Slide 17
2024 - RPS Consulting all rights reserved
Output
=== HARQ Process (TS 38.321 §5.4) ===
16 parallel stop-and-wait HARQ processes
RV sequence: 0 -> 2 -> 3 -> 1
HARQ[0] NEW TX: NDI=1 RV=0 data="PDU-DATA-A"
<< NACK (CRC fail) >>
HARQ[0] RETX #1: RV=2
<< NACK >>
HARQ[0] RETX #2: RV=3
<< ACK (combining success) >>
HARQ[0] ACK received
HARQ[0] NEW TX: NDI=0 RV=0 data="PDU-DATA-B"
<< ACK (first attempt) >>
HARQ[0] ACK received

## Slide 18
2024 - RPS Consulting all rights reserved
Key Concept Summary
HARQ
Reliability mechanism combining FEC with feedback-based retransmissions
Transport Block (TB)
Unit of data delivered from higher layers for transmission
HARQ Process
Independent transmission pipeline with unique ID and buffers
NDI
Flag distinguishing new TB from retransmission
Redundancy Version
Indicator for which coded bits are transmitted (0→2→3→1)
ACK/NACK
Receiver feedback controlling retransmissions
Soft Combining
Accumulating probability information across attempts
Incremental Redundancy
New parity per attempt, not repetition
Max Retx Limit
Threshold preventing indefinite retransmissions

## Slide 19
2024 - RPS Consulting all rights reserved
References

## Slide 20
2024 - RPS Consulting all rights reserved
Conclusion
HARQ is a critical closed-loop reliability system in 5G NR that ensures robust data delivery without compromising latency or spectral efficiency.
✓ Combines Physical Layer transmission with MAC layer control
✓ Uses incremental redundancy and soft combining for efficiency
✓ Parallel processes enable continuous high-throughput operation
✓ Forms the foundation for eMBB, URLLC, and mMTC services

## Slide 21
2024 - RPS Consulting all rights reserved
Thank You
                Presented By Group : 03
                1. Jayavarshini G
                2. Harshinie M
                3. Yuvaraj P
                4. Shreyash Bhatt
                5. Vikas Srivastava